## Slide 1: Agricultural-water use (AWU) Package for gsflow
Hyper-resolution modeling of Regional water use by agriculture

## Slide 2
Precipitation-Runoff Modeling (PRMS)
Streamflow Routing Package (SFR), LAK Package
Irrigation of PRMS HRUs or UZF cells
Watershed runoff
to streams
SW and GW supply
ET-based
SW and GW Demand

## Slide 3: Mode 1
SW diversion
Demand set using SFR2 input variable “FLOW”
(IRRIGATION SEGMENT)
Surface water (SW) irrigation using IRRIGATIONSEGMENT
Demand specified as SW diversions using TABFILES
ETa calculated by UZF/PRMS
(IUZFBND>0)
ETa calculated in AWU using efficiency factor
(IUZFBND<0)
Return flows (SW+GW) calculated by UZF/PRMS
Return
flows
Diversion
flows
TABFILE

## Slide 4: Mode 2
Surface water (SW) and groundwater (GW) irrigation using IRRIGATIONSEGMENT and IRRIGATIONWELL
Demand specified as SW diversions using TABFILES
SW diversion
Demand set using SFR2 (Tabfiles) input variable “FLOW”
(IRRIGATIONSEGMENT)
ETa calculated by UZF/PRMS
(IUZFBND>0)
ETa calculated in AGO using efficiency factor
(IUZFBND<0)
Return flows (SW+GW) calculated by UZF/PRMS
SW/GW
Irrigation
Demand set using AGO input variable “Q”
GW Demand set as SW shortfall
(SUPPLEMENTALWELL)
GW irrigation
(IRRIGATIONWELL)
TABFILE

## Slide 5: Mode 3
SW diversion set as Irrigation demand, and limited by the lesser of “FLOW” and Qseg
(IRRIGATIONSEGMENT)
Irrigation demand calculated using f(ETd-ETa)
(ETDEMAND)
ETa is calculated by UZF/PRMS
Diversion less than demand with supplemental GW rights
Apply SW and GW irrigation
Pumped GW
Externally (UZF) or internally (PRMS) calculated ETd
Diverted SW
Nonlinear iterations
Return flows (SW+GW) calculated by UZF/PRMS
GW pumping rate set as Irrigation demand, and limited by AGO input “Q”
GW Demand set as SW shortfall
(SUPPLEMENTALWELL)
No SW
GW right
GW irrigation
(IRRIGATIONWELL)
Demand set using ETDEMAND
GW irrigation set using SUPPLEMENTALWELL
Surface water (SW) and groundwater (GW) irrigation using IRRIGATIONSEGMENT and IRRIGATIONWELL

## Slide 6: AWU Package Input file structure
Well list can use TABFILES to change max constraint on pumping

## Slide 7: Test Model
Semi-arid
3500 acres of irrigated farms
Conjunctive use of SW and GW
2 year simulation
Mode 3
Irrigation schedule: every other week between April1st and September 30th

## Slide 8: Impacts of K on crop consumption- ET based demand
Chart: ETo and ETa for Kv=0.86 ft/day
Chart: ETo and ETa for Kv=4.32 ft/day
ETa is less than ETo due to irrigation schedule

## Slide 9: Cumulative SW and GW Irrigated Amounts for Different Field Hydraulic Conductivity Values
Chart: Cumulative Flows (CFS)

## Slide 10: Groundwater return flows
Chart: Percent Increase in deep percolation due to GW Return Flows

## Slide 11: Thanks you. Questions?