## Slide 1
Precipitation-Runoff Modeling (PRMS)
Streamflow Routing Package (SFR)
Irrigation on to PRMS HRUs or UZF cells
Drainage
to streams
SW diversions/GW pumping
For irrigation

## Slide 2
SW diversion
NIWR set using specified diversions in SFR input
A) Surface water (SW) irrigation using IRRIGATION_DIVERSION Option
ETa calculated by UZF/PRMS using soil-water balance
ETa calculated in AG using efficiency factor
Return flows (SW+GW) calculated by UZF/PRMS
Return
flows
Diversion
flows

## Slide 3
NIWR set using specified diversions in SFR input
B) Surface water (SW) and groundwater (GW) irrigation using IRRIGATION_DIVERSION and IRRIGATION_WELL
ETa calculated by UZF/PRMS
ETa calculated in AGO using efficiency factor
Return flows (SW+GW) calculated by UZF/PRMS
SW/GW
Irrigation
NIWR set using specified pumping rates in AG input
GW Demand set as SW shortfall
(SUPPLEMENTALWELL)
GW irrigation
(IRRIGATIONWELL)

## Slide 4
SW diversion set as Irrigation demand, and limited by the lesser of “FLOW” and Qseg
(IRRIGATIONSEGMENT)
C) Surface water (SW) and groundwater (GW) irrigation using IRRIGATION_SFR and IRRIGATION_WELL; demand calculated as ET deficit using ETDEMAND.
Irrigation demand calculated using f(ETd-ETa)
(ETDEMAND)
ETa is calculated by UZF/PRMS
Diversion less than demand with supplemental GW rights
Apply SW and GW irrigation
Pumped GW
Externally (UZF) or internally (PRMS) calculated ETd
Diverted SW
Nonlinear iterations
Return flows (SW+GW) calculated by UZF/PRMS
GW pumping rate set as Irrigation demand, and limited by AGO input “Q”
GW irrigation
(IRRIGATIONWELL)
GW Demand set as SW shortfall
(SUPPLEMENTALWELL)
No SW
GW right